## Slide 1: Charging SOP – How to Charge Safely and Efficiently (v1.0)
Why it matters:
Charging errors are the #1 cause of early downtime in EV fleets.
Standardizing routines avoids safety incidents, charger faults, and underutilization.
This SOP defines “who does what” and “how to charge right, every time.”
Notes: This could be tied directly to the Gannt chart tool.
I think it would be better to keep the "Deliverables" out of this section. So, we convey carefully the function of each stage.
Or we'll have to think of different ways to manage the complexity of this section.

## Slide 2: Roles and Responsibilities
Role | Responsibility
Driver / Operator | Perform pre-/post-charge checks and initiate charging.
Fleet Supervisor | Enforce schedule, review charger logs, manage exceptions.
Technician / Maintenance | Inspect, reset, and maintain charger functionality.
HSE Lead | Oversee electrical safety and emergency response.
Who does what?
Clear accountability reduces charger misuse and downtime.

## Slide 3: Pre-Charging & Charging Steps
How to Charge – Step by Step
Always check SOC and confirm the charge completed before moving the truck.
Checkpoint | Status
Inspect cable and plug for damage | ☐
Confirm charger ID and SOC level (<30%) | ☐
Ensure park brake & key off | ☐
Wear PPE, clear area | ☐
Checkpoint | Status
1️⃣ Plug in and authenticate (RFID/app) | ☐
2️⃣ Verify charging begins (display or telematics) | ☐
3️⃣ Monitor progress (SOC, power, ETA) | ☐
4️⃣ Stop at 100% (overnight) or 80% (mid-shift) | ☐
5️⃣ Unplug, coil cable, inspect bay | ☐
Pre-checks
Charging Procedure

## Slide 4: Faults & Emergencies
If Charging Fails or an Error Occurs
Never open charger cabinets or attempt repairs. Electrical safety first.
🚫 Charger unresponsive or flashing error
🚫 No initiation / interrupted session
🚫 Connector won’t unlock
🚫 Breaker trip or grid fault
1️⃣ Press STOP (if safe)
2️⃣ Do not force unplugging
3️⃣ Call maintenance / HSE contact
4️⃣ Tag charger “Out of Service”
5️⃣ Move truck to alternate bay
Driver
Fleet Supervisor
Technician
CPO Hotline
OEM
Escalation path:

## Slide 5: Smart Charging & Load Management
Manage the Power, Not Just the Plug
Smart charging ensures uptime without overloading the depot grid.
Checkpoint | Status
Follow charging window (e.g., 20:00–05:00) | ☐
Use telematics timers for load balancing | ☐
Avoid >25% fleet charging concurrently | ☐
Prioritize low-SOC and early departures | ☐
Track utilization via platform or dashboard | ☐

## Slide 6: Safety, Maintenance & Reporting
Keep It Safe, Keep It Working
Reliable charging starts with consistent routines.
✅ Dry ground only – no standing water
✅ Maintain 1.5 m clear zone
✅ No smoking or open flames
❌ Never repair or open chargers
❌ Never bypass RFID / safety systems
Frequency | Task | Owner
Weekly | Inspect cables, signage | Technician
Monthly | Firmware update | Vendor/CPO
Monthly | Electrical safety check | HSE Lead
Safety Do’s and Don’ts:
Maintenance Routine