## Slide 1: EV Driver Training SOP & Checklist (v1.0)
Objective: To Standardize safe and efficient EV truck operations:
Equip drivers to operate EVs safely and efficiently
Build consistent pre-/post-trip and charging habits
Reinforce escalation and safety awareness
Why it matters: EVs don’t drive like diesels. Without proper training, range, uptime, and safety all suffer. Drivers are your first line of defense against charging errors, downtime, and inefficient driving.
Notes: This could be tied directly to the Gannt chart tool.
I think it would be better to keep the "Deliverables" out of this section. So, we convey carefully the function of each stage.
Or we'll have to think of different ways to manage the complexity of this section.

## Slide 2: Training Overview
Module | Focus | Duration | Delivered by
1. EV Basics | How EVs differ from diesels – torque, SOC, battery systems | 30 min | OEM/Trainer
2. Energy Efficiency | Range management, regen braking, predictive driving | 45 min | Trainer
3. Charging Operations | Charging routines, safety, escalation | 30 min | Technician
4. Safety & Emergency | Responding to charger or vehicle faults | 30 min | HSE Lead
5. Route Familiarization | SOC planning, telematics monitoring | 45 min | Fleet Supervisor
Training modules overview.
Each driver completes classroom + hands-on modules before vehicle handover.

## Slide 3: Pre-Drive & On-Road Checklist
What to do before and during every shift
Checkpoint | Status
Check SOC, tire pressure, and cooling fluid | ☐
Confirm route and range buffer (≥20%) | ☐
Set Eco or Standard mode depending on load | ☐
Verify charging cable disconnected and stowed | ☐
Checkpoint
Accelerate smoothly — avoid sharp torque pulls
Use regenerative braking early and often
Maintain steady cruising (60–80 km/h)
Anticipate stops — predictive driving saves kWh
Avoid unnecessary idling (climate draws power)
Pre-drive
On-road

## Slide 4: Charging & Range Management
Charging Routines Drivers Must Know
1️⃣ When to charge
Follow assigned depot schedule
Plug in at ≤30% SOC for full overnight charge
Top-up mid-shift only if route or range requires
2️⃣ How to charge safely
Follow the Charging SOP
Inspect cables and confirm charger ID
Never force disconnects
3️⃣ What to report
Faulted sessions, slow charge rates, or range anomalies
SOC <10% after return
Use telematics or digital feedback form
Every charging action leaves a data trail — make sure it’s accurate.

## Slide 5: Safety & Fault Escalation
When Things Go Wrong
Safety first — never attempt repair or reset unless trained.
❌ Charger shows “Fault” or “Error” message
❌ Vehicle won’t start charging
❌ Connector stuck or won’t release
❌ Warning lights (battery temp, HV system, etc.)
Common scenarios:
1️⃣ Press STOP if safe
2️⃣ Don’t force disconnect
3️⃣ Report to supervisor
4️⃣ Tag charger “Out of Service”
5️⃣ Move to alternate bay if available
Immediate actions:

## Slide 6: Monitoring & Continuous Improvement
Driving Smarter Over Time
Smooth, safe, and smart driving is what makes electrification work.
Monitor energy (kWh/km) and regen % in telematics
Aim for target regen >30% and steady efficiency trends
Review monthly feedback with supervisor
Performance tracking:
Annual or after new vehicle/software updates
Retraining triggered by:
Consistently high consumption
Charger misuse
Fault escalation issues
Refresher training:

## Slide 7: Driver Certification & Sign-off
Final Step: Certify and Keep Improving
Linked documents: Charging SOP, Route & Duty Cycle Tool, Driver KPI Dashboard
Step | Verification | Responsible
Complete training modules | Attendance record | Trainer
Complete practical driving test | Route report + SOC verification | Supervisor
Pass post-training quiz | ≥80% score | Trainer
Certification issued | Valid for 12 months | Fleet Ops